## Slide 1: Chapter 4: Network Access
Instructor Materials
CCNA Routing and Switching
Introduction to Networks v6.0
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 4: Network Access

## Slide 2: Instructor Materials – Chapter 4 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the chapter
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide # 12
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2
Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 4: Network Access

## Slide 3: Chapter 4: Network Access
Introduction to Networks 6.0 Planning Guide
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 4: Network Access

## Slide 4: Chapter 4: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
4.0.1.2 | Class Activity | Managing the Network | Optional
4.1.2.4 | Lab | Identifying Network Devices and Cabling | Recommended
4.1.3.5 | Activity | Physical Layer Terminology | Recommended
4.2.1.7 | Activity | Copper Media Characteristics | Recommended
4.2.2.6 | Activities | T568A Cable Pinouts and T568B Cable Pinouts | Recommended
4.2.2.7 | Lab | Building an Ethernet Crossover Cable | Optional
4.2.3.7 | Activity | Fiber-optics Terminology | Recommended
4.2.4.4 | Packet Tracer | Connecting a Wired and Wireless LAN | Recommended
4.2.4.5 | Lab | Viewing Wired and Wireless NIC Information | Recommended
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4
Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 4: Network Access

## Slide 5: Chapter 4: Activities (Cont.)
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
4.4.4.3 | Activities | Part 1 and 2: Generic Frame Fields | Recommended
4.5.1.1 | Class Activity | Linked In! | Optional
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 5
Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 4: Network Access

## Slide 6: Chapter 4: Assessment
Students should complete Chapter 4, “Assessment” after completing Chapter 4.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 6
Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 4: Network Access

## Slide 7: Chapter 4: Best Practices
Prior to teaching Chapter 4, the instructor should:
Complete Chapter 4, “Assessment.”
The objectives of this chapter are:
  Identify device connectivity options.
  Describe the purpose and functions of the physical layer in the network.
  Describe basic principles of the physical layer standards.
  Identify the basic characteristics of copper cabling.
  Build a UTP cable used in Ethernet networks.
  Describe fiber optic cabling and its main advantages over other media.
  Connect devices using wired and wireless media.
  Describe the purpose and function of the data link layer in preparing communication for transmission on specific media.
  Compare the functions of logical topologies and physical topologies.
  Describe the basic characteristics of media access control methods on WAN and LAN topologies.
  Describe the characteristics and functions of the data link frame.
Notes: 7
Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 4: Network Access

## Slide 8: Chapter 4: Best Practices (Cont.)
  You may want to use a wireless router for the demonstration.
  Provide students with apps they can use at home to test download and upload speeds (for example: https://www.speakeasy.net/speedtest).
  Provide an example of bandwidth in terms of a water pipe. The larger the pipe, more water that can flow through it.
  Provide an example of throughput in terms of a water pipe. As a valve is opened, more water flows through.
  Show examples of different types of copper media. Hopefully you have saved some poorly made cables!
  Ask students to give examples of electromagnetic interference (for example: home wireless phones, microwaves, vacuum cleaner, etc.)
  Show that the wire pairs in UTP have a different number of twists to enhance cancellation.
  Demonstrate the types of UTP cables using a cable tester to show the wiring map.
  Make sure the students know that color matters in fiber optic cabling.
Notes: 8
Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 4: Network Access

## Slide 9: Chapter 4: Best Practices (Cont.)
  Use this video about undersea cable: https://www.youtube.com/watch?v=v1JEuzBkOD8
  Use this video about how undersea cables are laid: https://www.youtube.com/watch?v=XQVzU_YQ3IQ
  “A Frame is like a bed frame. It has a headboard (header) and footboard (trailer).”
  Begin an OSI Model Post-It Note exercise: Have each student take 10 post-it notes and write 5 key words for the physical layer and 5 key words for the data link layer. The words will be put in an envelope for later. Eventually, all 7 layers will be covered and students can exchange envelopes and properly align descriptions to the name of the layer.
  Describe how the physical and data link layers of the OSI model interoperate together.
  Explain that LLC and MAC work together as sublayers in the data link layer. LLC connects to Layer 3 and MAC connects to Layer 1.
  Draw examples of common physical WAN topologies on the board and have students generate pros and cons for each type.
  Full Mesh requires n*(n-1)/2 links for a full mesh (n=number of devices in full mesh).
Notes: 9
Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 4: Network Access

## Slide 10: Chapter 4: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at: https://www.netacad.com/group/communities/community-home
Best practices from around the world for teaching CCNA Routing and Switching. https://www.netacad.com/group/communities/ccna
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Students can enroll in Introduction to Packet Tracer (self-paced)
Notes: 10
Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 4: Network Access

## Slide 11
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 4: Network Access

## Slide 12: Chapter 4: Network Access
CCNA Routing and Switching
Introduction to Networks v6.0
Notes: Cisco Networking Academy Program
Introduction to Networks V6.0
Chapter 4: Network Access

## Slide 13: Chapter 4 - Sections & Objectives
4.1 Physical Layer Protocols
    Explain how physical layer protocols and services support communications across data networks.
    Identify device connectivity options.
    Describe the purpose and functions of the physical layer in the network.
    Describe basic principles of the physical layer standards.
4.2 Network Media
    Build a simple network using the appropriate media.
    Identify the basic characteristics of copper cabling.
    Build a UTP cable used in Ethernet networks. (scope - does not include cabling area discussion)
    Describe fiber optic cabling and its main advantages over other media.
    Connect devices using wired and wireless media.
Notes: 13
Cisco Networking Academy Program
Introduction to Networks V6.0
Chapter 4: Network Access

## Slide 14: Chapter 4 - Sections & Objectives (Cont.)
4.3 Data Link Layer Protocols
    Explain the role of the data link layer in supporting communications across data networks.
    Describe the purpose and function of the data link layer in preparing communication for transmission on specific media.
4.4 Media Access Control
    Compare media access control techniques and logical topologies used in networks.
    Compare the functions of logical topologies and physical topologies.
    Describe the basic characteristics of media access control methods on WAN topologies.
    Describe the basic characteristics of media access control methods on LAN topologies.
    Describe the characteristics and functions of the data link frame.
Notes: 14
Cisco Networking Academy Program
Introduction to Networks V6.0
Chapter 4: Network Access

## Slide 15: 4.1 Physical Layer Protocols
Notes: 4 – Network Access
4.1 – Physical Layer Protocols

## Slide 16: Physical Layer Connection Types of Connections
Before network communications can occur, a physical connection to a local network must be established.
A physical connection can be a wired connection using a cable or a wireless connection using radio waves.
Notes: 4.1 – Physical Layer Protocols
4.1.1 – Physical Layer Connection
4.1.1.1 – Types of Connections

## Slide 17: Physical Layer Connection Network Interface Cards
Network Interface Cards (NICs) connect a device to a network.
Used for a wired connection.
Wireless Local Area Network (WLAN) NICs are used for wireless connections.
Notes: 4.1 – Physical Layer Protocols
4.1.1 – Physical Layer Connection
4.1.1.2 – Network Interface Cards

## Slide 18: Purpose of the Physical Layer The Physical Layer
Provides the means to transport the bits that make up a data link layer frame across the network media.
Accepts a complete frame from the data link layer and encodes it as a series of signals that are transmitted onto the local media.
Encoded bits that comprise a frame are received by either an end device or an intermediate device.
Notes: 4.1 – Physical Layer Protocols
4.1.2 – Purpose of the Physical Layer
4.1.2.1 – The Physical Layer

## Slide 19: Purpose of the Physical Layer Physical Layer Media
Three basic forms of network media
Notes: 4.1 – Physical Layer Protocols
4.1.2 – Purpose of the Physical Layer
4.1.2.2 – Physical Layer Media

## Slide 20: Purpose of the Physical Layer Physical Layer Standards
International Organization for Standardization (ISO)
Telecommunications Industry Association/Electronic Industries Association (TIA/EIA)
International Telecommunication Union (ITU)
American National Standards Institute (ANSI)
Institute of Electrical and Electronics Engineers (IEEE)
Notes: 4.1 – Physical Layer Protocols
4.1.2 – Purpose of the Physical Layer
4.1.2.3 – Physical Layer Standards

## Slide 21: Purpose of the Physical Layer Lab - Identifying Network Devices and Cabling
Notes: 4.1 – Physical Layer Protocols
4.1.2 – Purpose of the Physical Layer
4.1.2.4 – Lab – Identifying Network Devices and Cabling

## Slide 22: Physical Layer Characteristics Functions
Encoding
  Method of converting a stream of data bits into a predefined "code”.
  Signaling Method
  Method of representing the bits.
  Physical layer standards must define what type of signal represents a "1" and what type of signal represents a "0”.
  Long pulse might represent a 1 whereas a short pulse represents a 0.
The transition occurs at the middle of each bit period.
Modulation is the process by which the characteristic of one wave (the signal) modifies another wave (the carrier).
Notes: 4.1 – Physical Layer Protocols
4.1.3 – Physical Layer Characteristics
4.1.3.1– Functions

## Slide 23: Physical Layer Characteristics Bandwidth
Capacity of a medium to carry data.
Digital bandwidth measures the amount of data that can flow from one place to another in a given amount of time.
Bandwidth is sometimes thought of as the speed that bits travel, however this is not accurate. In both 10Mb/s and 100Mb/s Ethernet, the bits are sent at the speed of electricity. The difference is the number of bits that are transmitted per second.
Notes: 4.1 – Physical Layer Protocols
4.1.3 – Physical Layer Characteristics
4.1.3.2 – Bandwidth

## Slide 24: Physical Layer Characteristics Throughput
Measure of the transfer of bits across the media over a given period of time.
Usually does not match the specified bandwidth in physical layer implementations due to many factors.
  Amount of traffic
  Type of traffic
  Latency created by network devices encountered between source and destination
Goodput is throughput minus traffic overhead for establishing sessions, acknowledgments, and encapsulation.
Notes: 4.1 – Physical Layer Protocols
4.1.3 – Physical Layer Characteristics
4.1.3.3– Throughput

## Slide 25: Physical Layer Characteristics Types of Physical Media
The figure shows different types of interfaces and ports available on a 1941 router.
Notes: 4.1 – Physical Layer Protocols
4.1.3 – Physical Layer Characteristics
4.1.3.4– Types of Physical Media

## Slide 26: 4.2 Network Media
Notes: 4 – Network Access
4.2 – Network Media

## Slide 27: Copper Cabling Characteristics of Copper Media
Transmitted on copper cables as electrical pulses.
Attenuation - the longer the signal travels, the more it deteriorates.
All copper media must follow strict distance limitations.
Electromagnetic interference (EMI) or radio frequency interference (RFI) - distorts and corrupts the data signals being carried by copper media.
  To counter copper cables wrapped in shielding.
Crosstalk - disturbance caused by the electric or magnetic fields of a signal on one wire to the signal in an adjacent wire.
  To cancel crosstalk opposing circuit wire pairs twisted together.
Notes: 4.2 – Network Media
4.2.1– Copper Cabling
4.2.1.1 – Characteristics of Copper Media

## Slide 28: Copper Cabling Copper Media
There are three main types of copper media used in networking.
Notes: 4.2 – Network Media
4.2.1– Copper Cabling
4.2.1.2 – Copper Media

## Slide 29: Copper Cabling Unshielded Twisted-Pair Cable
UTP cabling is the most common networking media.
  Terminated with RJ-45 connectors.
  Used for interconnecting network hosts with networking devices such as switches.
  Consists of four pairs of color-coded wires that have been twisted together to help protect against signal interference from other wires.
  Color codes aid in cable termination.
Notes: 4.2 – Network Media
4.2.1– Copper Cabling
4.2.1.3 – Unshielded Twisted-Pair Cable

## Slide 30: Copper Cabling Shielded Twisted-Pair (STP) Cable
STP provides better noise protection than UTP.
STP cable is significantly more expensive and difficult to install.
Uses an RJ-45 connector.
Combines the techniques of shielding to counter EMI and RFI, and wire twisting to counter crosstalk.
Uses four pairs of wires, each wrapped in a foil shield, which are then wrapped in an overall metallic braid or foil.
Notes: 4.2 – Network Media
4.2.1– Copper Cabling
4.2.1.4 – Shielded Twisted-Pair (STP) Cable

## Slide 31: Copper Cabling Coaxial Cable
Coax consists of:
  A copper conductor used to transmit the electronic signals.
  A layer of flexible plastic insulation surrounding a copper conductor.
  The insulating material is surrounded in a woven copper braid, or metallic foil, that acts as the second wire in the circuit and as a shield for the inner conductor.
  The entire cable is covered with a cable jacket to prevent minor physical damage.
UTP cable has essentially replaced coaxial cable in modern Ethernet installations but is used in:
  Wireless installations: Coaxial cables attach antennas to wireless devices.
  Cable Internet installations
Notes: 4.2 – Network Media
4.2.1– Copper Cabling
4.2.1.5 – Coaxial Cable

## Slide 32: Copper Cabling Copper Media Safety
Copper media are susceptible to fire and electrical hazards.
Notes: 4.2 – Network Media
4.2.1– Copper Cabling
4.2.1.6 – Copper Media Safety

## Slide 33: UTP Cabling Properties of UTP Cabling
Consists of four pairs of color-coded copper wires that have been twisted together and then encased in a flexible plastic sheath.
Small size can be advantageous during installation.
UTP cable does not use shielding to counter the effects of EMI and RFI.
  Cancellation: When two wires in an electrical circuit are placed close together, their magnetic fields are the exact opposite of each other and cancel out any outside EMI and RFI signals.
  Varies the number of twists per wire pair to further enhance the cancellation effect of a paired circuit.
Notice that the orange/orange white pair is twisted less than the blue/blue white pair. Each colored pair is twisted a different number of times.
Notes: 4.2 – Network Media
4.2.2 – UTP Cabling
4.2.2.1 – Properties of UTP Cabling

## Slide 34: UTP Cabling UTP Cabling Standards
UTP cabling conforms to the standards established by TIA/EIA.
  TIA/EIA-568 stipulates the cabling standards for LAN installations
Cat 3 Cable
  Used for voice communication
  Most often used for phone lines
Cat 5 and 5e Cable
  Used for data transmission
  Cat5 supports 100 Mb/s and can support 1000Mb/s, but it is not recommended
  Cat5e supports 1000 Mb/s
Cat 6 Cable
  Used for data transmission
  An added separator is between each pair of wires allowing it to function at higher speeds
  Support 1000 Mb/s – 10 Gb/s, though 10 Gb/s is not recommended
Notes: 4.2 – Network Media
4.2.2 – UTP Cabling
4.2.2.2 – UTP Cabling Standards

## Slide 35: UTP Cabling UTP Connectors
UTP cable terminated with an RJ-45 connector.
TIA/EIA-568 standard describes the wire color codes to pin assignments (pinouts) for Ethernet cables.
RJ-45 connector is the male component, crimped at the end of the cable.
Socket is the female component of a network device, wall, cubicle partition outlet, or patch panel.
Essential that all copper media terminations be of high quality to ensure optimum performance with current and future network technologies.
Notes: 4.2 – Network Media
4.2.2 – UTP Cabling
4.2.2.3 – UTP Connectors

## Slide 36: UTP Cabling Types of UTP Cable
Notes: 4.2 – Network Media
4.2.2 – UTP Cabling
4.2.2.4 – Types of UTP Cable

## Slide 37: UTP Cabling Testing UTP Cables
UTP Testing Parameters:
Wire map
Cable length
Signal loss due to attenuation
Crosstalk
Notes: 4.2 – Network Media
4.2.2 – UTP Cabling
4.2.2.5 – Testing UTP Cables

## Slide 38: UTP Cabling Lab - Building an Ethernet Crossover Cable
Notes: 4.2 – Network Media
4.2.2 – UTP Cabling
4.2.2.7 – Lab - Building an Ethernet Crossover Cable

## Slide 39: Fiber Optic Cabling Properties of Fiber Optic Cabling
Transmits data over longer distances and at higher bandwidths.
Transmit signals with less attenuation and is completely immune to EMI and RFI.
Used to interconnect network devices.
Flexible, but extremely thin, transparent strand of very pure glass, not much bigger than a human hair.
Bits are encoded on the fiber as light pulses.
Fiber-optic cabling is now being used in four types of industry:
  Enterprise Networks
  Fiber-to-the-Home (FTTH)
  Long-Haul Networks
  Submarine Cable Networks
Notes: 4.2 – Network Media
4.2.3 – Fiber Optic Cabling
4.2.3.1 – Properties of Fiber Optic Cabling

## Slide 40: Fiber Optic Cabling Fiber Media Cable Design
Jacket
Protects the fiber against abrasion, moisture, and other contaminants. Composition can vary depending on the cable usage.
Strengthening Material
Surrounds the buffer, prevents the fiber cable from being stretched when it is being pulled. Often the same material used to produce bulletproof vests.
Buffer
Used to help shield the core and cladding from damage.
Cladding
Tends to act like a mirror by reflecting light back in the core of the fiber. Keeps light in the core as it travels down the fiber.
Core
Light transmission element at the center of the optical fiber. Core is typically silica or glass. Light pulses travel through the fiber core.
Notes: 4.2 – Network Media
4.2.3 – Fiber Optic Cabling
4.2.3.2 – Fiber Media Cable Design

## Slide 41: Fiber Optic Cabling Types of Fiber Media
Notes: 4.2 – Network Media
4.2.3 – Fiber Optic Cabling
4.2.3.3 – Types of Fiber Media

## Slide 42: Fiber Optic Cabling Fiber-Optic Connectors
Light can only travel in one direction over optical fiber, two fibers are required to support the full duplex operation.
Straight-Tip (ST) Connectors
  One of the first connector types used.
  Locks securely with a “twist-on/twist-off”.
Subscriber Connector (SC) Connectors
  Referred to as square or standard connector.
  Uses a push-pull mechanism to ensure positive insertion.
  Used with multimode and single-mode fiber.
  Lucent Connector (LC) Simplex Connectors
  Smaller version of SC and popular due to size.
  Duplex Multimode LC Connectors
  Similar to LC but using a duplex connector.
Notes: 4.2 – Network Media
4.2.3 – Fiber Optic Cabling
4.2.3.4 – Fiber-Optic Connectors

## Slide 43: Fiber Optic Cabling Fiber-Optic Connectors (Cont.)
Fiber patch cords are required for interconnecting infrastructure devices.
Yellow jacket is for single-mode fiber cables
Orange (or aqua) for multimode fiber cables.
Fiber cables should be protected with a small plastic cap when not in use.
Notes: 4.2 – Network Media
4.2.3 – Fiber Optic Cabling
4.2.3.4 – Fiber-Optic Connectors

## Slide 44: Fiber Optic Cabling Testing Fiber Cables
Terminating and splicing fiber-optic cabling requires special training and equipment.
Three common types of fiber-optic termination and splicing errors are:
  Misalignment: The fiber-optic media are not precisely aligned to one another when joined.
  End gap: The media does not completely touch at the splice or connection.
  End finish: The media ends are not well polished, or dirt is present at the termination.
Can be field tested by shining a bright flashlight into one end of the fiber while observing the other end.
Optical Time Domain Reflectometer (OTDR) can be used to test each fiber-optic cable segment
Notes: 4.2 – Network Media
4.2.3 – Fiber Optic Cabling
4.2.3.5 – Testing Fiber Cables

## Slide 45: Fiber Optic Cabling Fiber versus Copper
Notes: 4.2 – Network Media
4.2.3 – Fiber Optic Cabling
4.2.3.6 – Fiber versus Copper

## Slide 46: Wireless Media Properties of Wireless Media
Wireless media carry electromagnetic signals that represent the binary digits of data communications using radio or microwave frequencies.
Wireless areas of concern:
  Coverage area: Construction materials used in buildings and structures, and the local terrain, will limit the coverage.
  Interference: Disrupted by such common devices as fluorescent lights, microwave ovens, and other wireless communications.
  Security: Devices and users, not authorized for access to the network, can gain access to the transmission.
  Shared medium: Only one device can send or receive at a time and the wireless medium is shared amongst all wireless users.
Notes: 4.2 – Network Media
4.2.4 – Wireless Media
4.2.4.1 – Properties of Wireless Media

## Slide 47: Wireless Media Types of Wireless Media
Wi-Fi: Standard IEEE 802.11
  Uses Carrier/Sense Multiple Access/Collision Avoidance (CSMA/CA).
  Wireless NIC must wait till channel is clear.
Bluetooth: Standard IEEE 802.15
  Wireless Personal Area Network (WPAN)
  Uses a device pairing process for distances 1 to 100 meters
WiMAX: Standard IEEE 802.16
  Worldwide Interoperability for Microwave Access
  Wireless broadband access.
Notes: 4.2 – Network Media
4.2.4 – Wireless Media
4.2.4.2 – Types of Wireless Media

## Slide 48: Wireless Media Wireless LAN
Wireless LAN requires the following network devices:
  Wireless Access Point (AP): Concentrates the wireless signals from users and connects to the existing copper-based network infrastructure, such as Ethernet.
  Wireless NIC adapters: Provide wireless communication capability to each network host.
  Home and small business wireless routers integrate the functions of a router, switch, and access point into one device.
Notes: 4.2 – Network Media
4.2.4 – Wireless Media
4.2.4.3 – Wireless LAN

## Slide 49: Wireless Media Packet Tracer - Connecting a Wired and Wireless LAN
Notes: 4.2 – Network Media
4.2.4 – Wireless Media
4.2.4.4 – Packet Tracer - Connecting a Wired and Wireless LAN

## Slide 50: Wireless Media Lab - Viewing Wired and Wireless NIC Information
Notes: 4.2 – Network Media
4.2.4 – Wireless Media
4.2.4.5 – Lab - Viewing Wired and Wireless NIC Information

## Slide 51: 4.3 Data Link Protocols
Notes: 4 – Network Access
4.3 – Data Link Protocols

## Slide 52: Purpose of the Data Link Layer The Data Link Layer
Notes: 4.3 – Data Link Layer Protocols
4.3.1 – Purpose of the Data Link Layer
4.3.1.1 – The Data Link Layer

## Slide 53: Purpose of the Data Link Layer The Data Link Layer (Cont.)
Layer 2 Data Link Addresses
Notes: 4.3 – Data Link Layer Protocols
4.3.1 – Purpose of the Data Link Layer
4.3.1.1 – The Data Link Layer

## Slide 54: Purpose of the Data Link Layer Data Link Sublayers
Data link layer is divided into two sublayers:
  Logical Link Control (LLC)
    Communicates with the network layer.
    Identifies which network layer protocol is being used for the frame.
    Allows multiple Layer 3 protocols, such as IPv4 and IPv6, to utilize the same network interface and media.
  Media Access Control (MAC)
    Defines the media access processes performed by the hardware.
    Provides data link layer addressing and access to various network technologies.
    Communicates with Ethernet to send and receive frames over copper or fiber-optic cable.
    Communicates with wireless technologies such as Wi-Fi and Bluetooth.
Notes: 4.3 – Data Link Layer Protocols
4.3.1 – Purpose of the Data Link Layer
4.3.1.2 – Data Link Sublayers

## Slide 55: Purpose of the Data Link Layer Media Access Control
As packets travel from the source host to the destination host, they travel over different physical networks.
Physical networks can consist of different types of physical media such as copper wires, optical fibers, and wireless consisting of electromagnetic signals, radio and microwave frequencies, and satellite links.
Notes: 4.3 – Data Link Layer Protocols
4.3.1 – Purpose of the Data Link Layer
4.3.1.3 – Media Access Control

## Slide 56: Purpose of the Data Link Layer Providing Access to Media
At each hop along the path, a router:
  Accepts a frame from a medium
  De-encapsulates the frame
  Re-encapsulates the packet into a new frame
  Forwards the new frame appropriate to the medium of that segment
Notes: 4.3 – Data Link Layer Protocols
4.3.1 – Purpose of the Data Link Layer
4.3.1.4 – Providing Access to Media

## Slide 57: Purpose of the Data Link Layer Data Link Layer Standards
Engineering organizations that define open standards and protocols that apply to the network access layer include:
  Institute of Electrical and Electronics Engineers (IEEE)
  International Telecommunication Union (ITU)
  International Organization for Standardization (ISO)
  American National Standards Institute (ANSI)
Notes: 4.3 – Data Link Layer Protocols
4.3.1 – Purpose of the Data Link Layer
4.3.1.5 – Data Link Layer Standards

## Slide 58: 4.4 Media Access Control
Notes: 4 – Network Access
4.4 – Media Access Control

## Slide 59: Topologies Controlling Access to the Media
Media access control is the equivalent of traffic rules that regulate the entrance of motor vehicles onto a roadway.
The absence of any media access control would be the equivalent of vehicles ignoring all other traffic and entering the road without regard to the other vehicles.
However, not all roads and entrances are the same. Traffic can enter the road by merging, by waiting for its turn at a stop sign, or by obeying signal lights. A driver follows a different set of rules for each type of entrance.
Sharing the Media
Notes: 4.4 – Media Access Control
4.4.1 – Topologies
4.4.1.1 – Controlling Access to the Media

## Slide 60: Topologies Physical and Logical Topologies
Physical topology - Refers to the physical connections and identifies how end devices and infrastructure devices such as routers, switches, and wireless access points are interconnected.
Notes: 4.4 – Media Access Control
4.4.1 – Topologies
4.4.1.2 – Physical and Logical Topologies

## Slide 61: Topologies Physical and Logical Topologies (Cont.)
Logical Topology: Refers to the way a network transfers frames from one node to the next. These logical signal paths are defined by data link layer protocols.
Notes: 4.4 – Media Access Control
4.4.1 – Topologies
4.4.1.2 – Physical and Logical Topologies

## Slide 62: WAN Topologies Common Physical WAN Topologies
Point-to-Point - Permanent link between two endpoints.
Hub and Spoke - A central site interconnects branch sites using point-to-point links.
Mesh - Provides high availability, but requires that every end system be interconnected to every other system. Administrative and physical costs can be significant.
Notes: 4.4 – Media Access Control
4.4.2 – WAN Topologies
4.4.2.1 – Common Physical WAN Topologies

## Slide 63: WAN Topologies Physical Point-to-Point Topology
Frames are placed on the media by the node at one end and taken from the media by the node at the other end of the point-to-point circuit.
Notes: 4.4 – Media Access Control
4.4.2 – WAN Topologies
4.4.2.2 – Physical Point-to-Point Topology

## Slide 64: WAN Topologies Logical Point-to-Point Topology
  End nodes communicating in a point-to-point network can be physically connected via a number of intermediate devices.
  However, the use of physical devices in the network does not affect the logical topology.
  The logical connection between nodes forms what is called a virtual circuit.
Notes: 4.4 – Media Access Control
4.4.2 – WAN Topologies
4.4.2.3 – Logical Point-to-Point Topology

## Slide 65: WAN Topologies Logical Point-to-Point Topology (Cont.)
Notes: 4.4 – Media Access Control
4.4.2 – WAN Topologies
4.4.2.3 – Logical Point-to-Point Topology

## Slide 66: LAN Topologies Physical LAN Topologies
Star - End devices are connected to a central intermediate device. Use Ethernet switches.
Extended Star - Additional Ethernet switches interconnect other star topologies.
Bus - Used in legacy networks. All end systems are chained to each other and terminated in some form on each end. Switches are not required to interconnect the end devices. Bus topologies using coax cables were used in legacy Ethernet networks because it was inexpensive and easy to set up.
Ring - End systems are connected to their respective neighbor forming a ring. Unlike the bus topology, the ring does not need to be terminated. Ring topologies were used in legacy Fiber Distributed Data Interface (FDDI) and Token Ring networks.
Notes: 4.4 – Media Access Control
4.4.3 – LAN Topologies
4.4.3.1 – Physical LAN Topologies

## Slide 67: LAN Topologies Half and Full Duplex
Half-Duplex Communication
  Both devices can transmit and receive on the media but cannot do so simultaneously.
  Used in legacy bus topologies and with Ethernet hubs.
  WLANs also operate in half-duplex.
Notes: 4.4 – Media Access Control
4.4.3 – LAN Topologies
4.4.3.2– Half and Full Duplex

## Slide 68: LAN Topologies Half and Full Duplex (Cont.)
Full-Duplex Communication
  Both devices can transmit and receive on the media at the same time.
  Data link layer assumes that the media is available for transmission for both nodes at any time.
  Ethernet switches operate in full-duplex mode by default, but can operate in half-duplex if connecting to a device such as an Ethernet hub.
Notes: 4.4 – Media Access Control
4.4.3 – LAN Topologies
4.4.3.2– Half and Full Duplex

## Slide 69: LAN Topologies Media Access Control Methods
Contention-Based Access
  Nodes operate in half-duplex.
  Compete for the use of the medium.
  Only one device can send at a time.
Notes: 4.4 – Media Access Control
4.4.3 – LAN Topologies
4.4.3.3– Media Access Control Methods

## Slide 70: LAN Topologies Media Access Control Methods (Cont.)
Controlled Access
  Each node has its own time to use the medium.
  Legacy Token Ring LANs are an example
Notes: 4.4 – Media Access Control
4.4.3 – LAN Topologies
4.4.3.3– Media Access Control Methods

## Slide 71: LAN Topologies Contention-based Access - CSMA/CD
Carrier Sense Multiple Access/Collision Detection (CSMA/CD) process is used in half-duplex Ethernet LANs.
  If two devices transmit at the same time, a collision will occur.
  Both devices will detect the collision on the network.
  Data sent by both devices will be corrupted and will need to be resent.
1
2
3
Notes: 4.4 – Media Access Control
4.4.3 – LAN Topologies
4.4.3.4– Contention-based Access - CSMA/CD

## Slide 72: LAN Topologies Contention-based Access - CSMA/CA
CSMA/CA
  Uses a method to detect if the media is clear.
  Does not detect collisions but attempts to avoid them by waiting before transmitting.
Note: Ethernet LANs using switches do not use a contention-based system because the switch and the host NIC operate in full-duplex mode.
Notes: 4.4 – Media Access Control
4.4.3 – LAN Topologies
4.4.3.5– Contention-based Access - CSMA/CA

## Slide 73: Data Link Frame The Frame
Each frame type has three basic parts:
  Header
  Data
  Trailer
Structure of the frame and the fields contained in the header and trailer depend on Layer 3 protocol.
Notes: 4.4 – Media Access Control
4.4.4 – Data Link Frame
4.4.4.1– The Frame

## Slide 74: Data Link Frame Frame Fields
Frame start and stop indicator flags - Identifies the beginning and end limits of the frame.
Addressing - Indicates the source and destination nodes.
Type - Identifies the Layer 3 protocol in the data field.
Control - Identifies special flow control services such as QoS.
Data - Contains the frame payload (i.e., packet header, segment header, and the data).
Notes: 4.4 – Media Access Control
4.4.4 – Data Link Frame
4.4.4.2– Frame Fields

## Slide 75: Data Link Frame Layer 2 Addresses
Each data link frame contains the source data link address of the NIC card sending the frame, and the destination data link address of the NIC card receiving the frame.
Notes: 4.4 – Media Access Control
4.4.4 – Data Link Frame
4.4.4.4– Layer 2 Addresses

## Slide 76: Data Link Frame LAN and WAN Frames
Layer 2 protocol used for a topology is determined by the technology.
Data link layer protocols include:
  Ethernet
  802.11 Wireless
  Point-to-Point Protocol (PPP)
  HDLC
  Frame Relay
Notes: 4.4 – Media Access Control
4.4.4 – Data Link Frame
4.4.4.5 – LAN and WAN Frames

## Slide 77: 4.5 Chapter Summary
Notes: 4 – Network Access
4.5 – Summary

## Slide 78: Conclusion Chapter 4: Network Access
Explain how physical layer protocols and services support communications across data networks.
Build a simple network using the appropriate media.
Explain the role of the data link layer in supporting communications across data networks.
Compare media access control techniques and logical topologies used in networks.
Notes: 4.5 – Summary
4.5.1 – Conclusion
4.5.1.2 Chapter 4: Network Access

## Slide 79: Section 4.1 New Terms and Commands
Telecommunications Industry Association/Electronic Industries Association (TIA/EIA) International Telecommunication Union (ITU) American National Standards Institute (ANSI) Institute of Electrical and Electronics Engineers (IEEE) Manchester encoding bandwidth throughput goodput |  | 
Notes: New Terms and Commands

## Slide 80: Section 4.2 New Terms and Commands
electromagnetic interference (EMI) radio frequency interference (RFI) crosstalk unshielded twisted-pair shielded twisted-pair coaxial cable coax fiber-optic cable | 
Notes: New Terms and Commands

## Slide 81: Section 4.3 New Terms and Commands
Logical Link Control (LLC) Media Access Control (MAC) | 
Notes: New Terms and Commands

## Slide 82: Section 4.4 New Terms and Commands
physical topology logical topology virtual circuit half-duplex full-duplex Carrier Sense Multiple Access/Collision Detection (CSMA/CD) Carrier Sense Multiple Access/Collision Avoidance (CSMA/CA) | 
Notes: New Terms and Commands