## Slide 1: Chapter 8: Subnetting IP Networks
Instructor Materials
CCNA Routing and Switching
Introduction to Networks v6.0
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 8: Subnetting IP Networks

## Slide 2: Instructor Materials – Chapter 8 Planning Guide
This PowerPoint deck is divided in two parts:
Instructor Planning Guide
  Information to help you become familiar with the chapter
  Teaching aids
Instructor Class Presentation
  Optional slides that you can use in the classroom
  Begins on slide # 13
Note: Remove the Planning Guide from this presentation before sharing with anyone.
Notes: 2

## Slide 3: Chapter 8: Subnetting IP Networks
Introduction to Networks 6.0 Planning Guide
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 8: Subnetting IP Networks

## Slide 4: Chapter 8: Activities
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
8.0.1.2 | Class Activity | Call Me! | Optional
8.1.2.4 | Video Demonstration | The Subnet Mask | Recommended
8.1.2.5 | Video Demonstration | Subnetting with the Magic Number | Recommended
8.1.2.8 | Video Demonstration | Creating Two Equal-sized Subnets | Recommended
8.1.2.11 | Video Demonstration | Creating Four Equal-sized Subnets | Recommended
8.1.2.12 | Video Demonstration | Creating Eight Equal-sized Subnets | Recommended
8.1.3.4 | Video Demonstration | Creating One Hundred Equal-sized Subnets | Recommended
8.1.3.6 | Video Demonstration | Subnetting Across Multiple Octets | Recommended
8.1.4.4 | Interactive Activity | Calculate the Subnet Mask | Recommended
8.1.4.5 | Interactive Activity | Determine the Number of Bits to Borrow | Recommended
8.1.4.6 | Lab | Calculating IPv4 Subnets | Optional
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 4

## Slide 5: Chapter 8: Activities (Cont.)
What activities are associated with this chapter?
Page # | Activity Type | Activity Name | Optional?
8.1.4.7 | Packet Tracer | Subnetting Scenario | Optional
8.1.4.8 | Lab | Designing and Implementing a Subnetted IPv4 Addressing Scheme | Recommended
8.1.5.4 | Video Demonstration | Basic VLSM | Recommended
8.1.5.7 | Video Demonstration | VLSM Example | Recommended
8.1.5.8 | Interactive Activity 1 and 2 | Practicing VLSM | Recommended
8.2.1.4 | Packet Tracer | Designing and Implementing a VLSM Addressing Scheme | Recommended
8.2.1.5 | Lab | Designing and Implementing a VLSM Addressing Scheme | Optional
8.3.1.4 | Packet Tracer | Implementing a Subnetted IPv6 Addressing Scheme | Optional
8.4.1.1 | Class Activity | Can you call me now? | Optional
8.4.1.2 | Packet Tracer | Skills Integration Challenge | Recommended
The password used in the Packet Tracer activities in this chapter is: PT_ccna5
Notes: 5

## Slide 6: Chapter 8: Assessment
Students should complete Chapter 8, “Assessment” after completing Chapter 8.
Quizzes, labs, Packet Tracers and other activities can be used to informally assess student progress.
Notes: 6

## Slide 7: Chapter 8: Best Practices
Prior to teaching Chapter 8, the instructor should:
Complete Chapter 8, “Assessment.”
The objectives of this chapter are:
  Explain how subnetting segments a network to enable better communication.
  Explain how to calculate IPv4 subnets for a /24 prefix.
  Explain how to calculate IPv4 subnets for a /16 and /8 prefix.
  Given a set of requirements for subnetting, implement an IPv4 addressing scheme.
  Explain how to create a flexible addressing scheme using variable length subnet masking (VLSM).
  Implement a VLSM addressing scheme.
  Explain how to implement IPv6 address assignments in a business network..
Notes: 7

## Slide 8: Chapter 8: Best Practices (Cont.)
  Ensure that students are familiar with binary and hexadecimal before beginning this chapter.
Direct the students to the binary game located at this URL to test their binary-decimal conversion skills: https://learningnetwork.cisco.com/docs/DOC-1803
  Explain the importance of designing, implementing, and managing an effective IP addressing plan so that networks can operate effectively and efficiently.
  Explain the hierarchical structure of an IP address by using analogies (for example, mailing address and phone numbers).
  Point out that subnetting is done in IPv6 to create a logical and hierarchical addressing design, not to conserve addresses.
  Demonstrate how to calculate subnets and hosts using the Magic number shortcut (see video 8.1.2.5).
Notes: 8

## Slide 9: Chapter 8: Best Practices (Cont.)
  Encourage students to see patterns and find shortcuts for subnetting.
  Provide practice scenarios for the students to use the formula 2^n (n= number of bits borrowed) to calculate subnets.
  The formula, 2^n-2, is required to calculate the usable number of addresses.
  Remind students that the first and last address of each subnet cannot be used as host addresses. First is network id and last is broadcast for the subnetwork.
  Google to find practice problems available in the “IP Addressing and Subnetting Workbook, by Robb Jones” (student and instructor versions are available in PDF format).
  In addition to theoretical subnetting problems, students should complete the labs that require not only designing and calculating addressing schemes, but also applying addresses to devices on a network.
Notes: 9

## Slide 10: Chapter 8: Best Practices (Cont.)
  Demonstrate how addresses are wasted in traditional subnetting by using one subnet mask for the whole network.
Explain how to conserve addresses using VLSM. Use VLSM to solve the wasted addresses issue on the WAN connections. VLSM is subnetting a subnet to create subnets with different numbers of hosts.
Notes: 10

## Slide 11: Chapter 8: Additional Help
For additional help with teaching strategies, including lesson plans, analogies for difficult concepts, and discussion topics, visit the CCNA Community at: https://www.netacad.com/group/communities/community-home
Best practices from around the world for teaching CCNA Routing and Switching. https://www.netacad.com/group/communities/ccna
If you have lesson plans or resources that you would like to share, upload them to the CCNA Community in order to help other instructors.
Students can enroll in Introduction to Packet Tracer (self-paced).
Notes: 11

## Slide 13: Chapter 8: Subnetting IP Networks
CCNA Routing and Switching
Introduction to Networks v6.0
Notes: Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 8: Subnetting IP Networks

## Slide 14: Chapter 8 - Sections & Objectives
8.1 Subnetting an IPv4 Network
  Implement an IPv4 addressing scheme to enable end-to-end connectivity in a small to medium-sized business network.
  Explain how subnetting segments a network to enable better communication.
  Explain how to calculate IPv4 subnets for a /24 prefix.
  Explain how to calculate IPv4 subnets for a /16 and /8 prefix.
  Given a set of requirements for subnetting, implement an IPv4 addressing scheme.
  Explain how to create a flexible addressing scheme using variable length subnet masking (VLSM).
8.2 Addressing Schemes
  Given a set of requirements, implement a VLSM addressing scheme to provide connectivity to end users in a small to medium-sized network.
  Implement a VLSM addressing scheme.
Notes: 14
Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 8: Subnetting IP Networks

## Slide 15: Chapter 8 - Sections & Objectives (Cont.)
8.3 Address Schemes
  Explain design considerations for implementing IPv6 in a business network.
  Explain how to implement IPv6 address assignments in a business network.
Notes: 15
Cisco Networking Academy Program
Introduction to Networks v6.0
Chapter 8: Subnetting IP Networks

## Slide 16: 8.1 Subnetting an IPv4 Network
Notes: 8 – Subnetting IP Networks
8.1 – Subnetting an IPv4 Network

## Slide 17: Network Segmentation Broadcast Domains
Devices use broadcasts in an Ethernet LAN to locate:
  Other devices - Address Resolution Protocol (ARP) which sends Layer 2 broadcasts to a known IPv4 address on the local network to discover the associated MAC address.
  Services – Dynamic Host Configuration Protocol (DHCP) which sends broadcasts on the local network to locate a DHCP server.
Switches propagate broadcasts out all interfaces except the interface on which it was received.
Notes: 8.1 – Subnetting an IPv4 Network
8.1.1 – Network Segmentation
8.1.1.1 – Broadcast Domains

## Slide 18: Network Segmentation Problems with Large Broadcast Domains
Hosts can generate excessive broadcasts and negatively affect the network.
  Slow network operations due to the significant amount of traffic it can cause.
  Slow device operations because a device must accept and process each broadcast packet.
Solution: Reduce the size of the network to create smaller broadcast domains. These smaller network spaces are called subnets.
Broadcast in LAN 1 contained in 1 subnet
Broadcast in LAN 2 contained in 1 subnet
One Broadcast Domain
Notes: 8.1 – Subnetting an IPv4 Network
8.1.1 – Network Segmentation
8.1.1.2 – Problems with Large Broadcast Domains

## Slide 19: Network Segmentation Reasons for Subnetting
Reduces overall network traffic and improves network performance.
Enables an administrator to implement security policies such as which subnets are allowed or not allowed to communicate together.
Subnetting by Location
Communicating between
Networks
Subnetting by Device Type
Notes: 8.1 – Subnetting an IPv4 Network
8.1.1 – Network Segmentation
8.1.1.2 – Reasons for Subnetting

## Slide 20: Subnetting an IPv4 Network Octet Boundaries
Prefix length and the subnet mask are different ways of identifying the network portion of an address.
Subnets are created by borrowing host bits for network bits.
More host bits borrowed, the more subnets that can be defined.
Networks are most easily subnetted at the
octet boundary of /8, /16, and /24
Notes: 8.1 – Subnetting an IPv4 Network
8.1.2 – Subnetting an IPv4 Network
8.1.2.1 – Octet Boundaries

## Slide 21: Subnetting an IPv4 Network Subnetting on the Octet Boundary
Subnetting Network 10.x.0.0/16
Define up to 256 subnets with each subnet capable of connecting 65,534 hosts.
First two octets identify the network portion while the last two octets are for host IP addresses.
Notes: 8.1 – Subnetting an IPv4 Network
8.1.2 – Subnetting an IPv4 Network
8.1.2.2 – Subnetting on the Octet Boundary

## Slide 22: Subnetting an IPv4 Network Subnetting on the Octet Boundary (Cont.)
Subnetting Network 10.x.x.0/24
Define 65,536 subnets each capable of connecting 254 hosts.
/24 boundary is very popular in subnetting because of number of hosts.
Notes: 8.1 – Subnetting an IPv4 Network
8.1.2 – Subnetting an IPv4 Network
8.1.2.2 – Subnetting on the Octet Boundary

## Slide 23: Subnetting an IPv4 Network Classless Subnetting
Subnets can borrow bits from any host bit position to create other masks.
Subnetting a /24 Network
Notes: 8.1 – Subnetting an IPv4 Network
8.1.2 – Subnetting an IPv4 Network
8.1.2.3 – Classless Subnetting

## Slide 24: Subnetting an IPv4 Network Video Demonstration – The Subnet Mask
Subnetting in Binary
ANDING
  Convert IP address and Subnet Mask to Binary (line up vertically like an addition problem)
  Logically AND (1 and 1 = 1, all other combinations = 0)
  Result is network address for original IP address
Classful Subnetting
  Class A /8 255.0.0.0
  Class B /16 255.255.0.0
  Class C /24 255.255.255.0
Notes: 8.1 – Subnetting an IPv4 Network
8.1.2 – Subnetting an IPv4 Network
8.1.2.4 – Video – The Subnet Mask

## Slide 25: Subnetting an IPv4 Network Video Demonstration – The Subnet Mask (Cont.)
Notes: 8.1 – Subnetting an IPv4 Network
8.1.2 – Subnetting an IPv4 Network
8.1.2.4 – Video – The Subnet Mask

## Slide 26: Subnetting an IPv4 Network Video Demonstration – Subnetting with the Magic Number
Magic number technique used to calculate subnets
Magic number is simply the place value of the last one in the subnet mask
/25 11111111.11111111.11111111.10000000 magic number = 128
/26 11111111.11111111.11111111.11000000 magic number = 64
/27 11111111.11111111.11111111.11100000 magic number = 32
Notes: 8.1 – Subnetting an IPv4 Network
8.1.2 – Subnetting an IPv4 Network
8.1.2.5 – Video – Subnetting with the Magic Number

## Slide 27: Subnetting an IPv4 Network Video Demonstration – Subnetting with the Magic Number (Cont.)
Notes: 8.1 – Subnetting an IPv4 Network
8.1.2 – Subnetting an IPv4 Network
8.1.2.5 – Video – Subnetting with the Magic Number

## Slide 28: Subnetting an IPv4 Network Video Demonstration – Subnetting with the Magic Number (Cont.)
Notes: 8.1 – Subnetting an IPv4 Network
8.1.2 – Subnetting an IPv4 Network
8.1.2.5 – Video – Subnetting with the Magic Number

## Slide 29: Subnetting an IPv4 Network Classless Subnetting Example
Notes: 8.1 – Subnetting an IPv4 Network
8.1.2 – Subnetting an IPv4 Network
8.1.2.6 – Classless Subnetting Example

## Slide 30: Subnetting an IPv4 Network Creating 2 Subnets
/25 Subnetting Topology
Notes: 8.1 – Subnetting an IPv4 Network
8.1.2 – Subnetting an IPv4 Network
8.1.2.7 – Creating 2 Subnets

## Slide 31: Subnetting an IPv4 Network Video Demonstration – Creating Two Equal-sized Subnets (/25)
Create 2 Equal-sized Subnets from 192.168.1.0 /24
Subnet Mask - 11111111.11111111.11111111.10000000
Magic Number = 128
192.168.1.0 /25 (start at 0)
192.168.1.128 /25 (Add 128)
Notes: 8.1 – Subnetting an IPv4 Network
8.1.2 – Subnetting an IPv4 Network
8.1.2.8 – Video Demonstration – Creating Two Equal-sized Subnets (/25)

## Slide 32: Subnetting an IPv4 Network Subnetting Formulas
Calculate Number of Subnets Formula
Subnetting a /24 Network
Notes: 8.1 – Subnetting an IPv4 Network
8.1.2 – Subnetting an IPv4 Network
8.1.2.9 – Subnetting Formulas

## Slide 33: Subnetting an IPv4 Network Subnetting Formulas (Cont.)
Calculate Number of Hosts Formula
Calculating the Number of Hosts
Notes: 8.1 – Subnetting an IPv4 Network
8.1.2 – Subnetting an IPv4 Network
8.1.2.9 – Subnetting Formulas

## Slide 34: Subnetting an IPv4 Network Creating 4 Subnets
/26 Subnetting Topology
Notes: 8.1 – Subnetting an IPv4 Network
8.1.2 – Subnetting an IPv4 Network
8.1.2.10 – Creating 4 Subnets

## Slide 35: Subnetting an IPv4 Network Creating 4 Subnets (Cont.)
/26 Subnetting Topology
Notes: 8.1 – Subnetting an IPv4 Network
8.1.2 – Subnetting an IPv4 Network
8.1.2.10 – Creating 4 Subnets

## Slide 36: Subnetting an IPv4 Network Creating 4 Subnets (Cont.)
/26 Subnetting Topology
Notes: 8.1 – Subnetting an IPv4 Network
8.1.2 – Subnetting an IPv4 Network
8.1.2.10 – Creating 4 Subnets

## Slide 37: Subnetting an IPv4 Network Video Demonstration – Creating Four Equal-sized Subnets (/26)
Create 4 Equal-sized Subnets from 192.168.1.0 /24
Subnet Mask in Binary – 11111111.11111111.11111111.11000000
2^2 = 4 Subnets
Magic Number = 64
192.168.1.0 /26
192.168.1.64 /26
192.168.1.128 /26
192.168.1.192 /26
Notes: 8.1 – Subnetting an IPv4 Network
8.1.2 – Subnetting an IPv4 Network
8.1.2.11 – Video Demonstration – Creating Four Equal-sized Subnets (/26)

## Slide 38: Subnetting an IPv4 Network Video Demonstration – Creating Eight Equal-sized Subnets (/27)
Create 8 Equal-sized Subnets from 192.168.1.0 /24
Borrow 3 bits – 11111111.11111111.11111111.11100000
Magic Number = 32
192.168.1.0 /27 (Start at 0)
192.168.1.32 /27 (Add 32 to previous network)
192.168.1.64 /27 (Add 32)
192.168.1.96 /27 (Add 32)
192.168.1.128 /27 (Add 32)
192.168.1.160 /27 (Add 32)
192.168.1.192 /27 (Add 32)
192.168.1.224 /27 (Add 32)
Notes: 8.1 – Subnetting an IPv4 Network
8.1.2 – Subnetting an IPv4 Network
8.1.2.12 – Video Demonstration – Creating Eight Equal-sized Subnets (/27)

## Slide 39: Subnetting a /16 and /8 Prefix Creating Subnets with a /16 prefix
Notes: 8.1 – Subnetting an IPv4 Network
8.1.3 – Subnetting a /16 and /8 Prefix
8.1.3.1 – Creating Subnets with a /16 prefix

## Slide 40: Subnetting a /16 and /8 Prefix Creating 100 Subnets with a /16 prefix
Notes: 8.1 – Subnetting an IPv4 Network
8.1.3 – Subnetting a /16 and /8 Prefix
8.1.3.2 – Creating 100 Subnets with a /16 prefix

## Slide 41: Subnetting a /16 and /8 Prefix Calculating the Hosts
Notes: 8.1 – Subnetting an IPv4 Network
8.1.3 – Subnetting a /16 and /8 Prefix
8.1.3.3 – Calculating the Hosts

## Slide 42: Subnetting a /16 and /8 Prefix Video Demonstration – Creating One Hundred Equal-sized Subnets
An enterprise network requires 100 equal-sized subnets starting from 172.16.0.0/16
  New Subnet Mask
    11111111.11111111.11111110.00000000
  2^7 = 128 Subnets
  2^9 = 512 hosts per subnet
  Magic Number = 2
  172.16.0.0 /23
  172.16.2.0 /23
  172.16.4.0 /23
  172.16.6.0 /23
  …
  172.16.254.0 /23
Notes: 8.1 – Subnetting an IPv4 Network
8.1.3 – Subnetting a /16 and /8 Prefix
8.1.3.4 – Video Demonstration – Creating One Hundred Equal-sized Subnets

## Slide 43: Subnetting a /16 and /8 Prefix Creating 1000 Subnets with a /8 Network
Notes: 8.1 – Subnetting an IPv4 Network
8.1.3 – Subnetting a /16 and /8 Prefix
8.1.3.5 – Creating 1000 Subnets with a /8 Network

## Slide 44: Subnetting a /16 and /8 Prefix Creating 1000 Subnets with a /8 Network (Cont.)
Notes: 8.1 – Subnetting an IPv4 Network
8.1.3 – Subnetting a /16 and /8 Prefix
8.1.3.5 – Creating 1000 Subnets with a /8 Network

## Slide 45: Subnetting a /16 and /8 Prefix Video Demonstration – Subnetting Across Multiple Octets
New Challenge Problem: Create over 300 Equal-sized Subnets of 20,000 Hosts each starting from 10.0.0.0/8
Notes: 8.1 – Subnetting an IPv4 Network
8.1.3 – Subnetting a /16 and /8 Prefix
8.1.3.6 – Video Demonstration – Subnetting Across Multiple Octets

## Slide 46: Subnetting to Meet Requirements Subnetting Based on Host Requirements
Notes: 8.1 – Subnetting an IPv4 Network
8.1.4 – Subnetting to Meet Requirements
8.1.4.1 – Subnetting Based on Host Requirements

## Slide 47: Subnetting to Meet Requirements Subnetting Based On Network Requirements
Host devices used by employees in the Engineering department in one network and Management in a separate network.
Notes: 8.1 – Subnetting an IPv4 Network
8.1.4 – Subnetting to Meet Requirements
8.1.4.2 – Subnetting Based On Network Requirements

## Slide 48: Subnetting to Meet Requirements Network Requirement Example
Notes: 8.1 – Subnetting an IPv4 Network
8.1.4 – Subnetting to Meet Requirements
8.1.4.3 – Network Requirement Example

## Slide 49: Subnetting to Meet Requirements Network Requirement Example (Cont.)
Notes: 8.1 – Subnetting an IPv4 Network
8.1.4 – Subnetting to Meet Requirements
8.1.4.3 – Network Requirement Example

## Slide 50: Subnetting to Meet Requirements Lab – Calculating IPv4 Subnets
Notes: 8.1 – Subnetting an IPv4 Network
8.1.4 – Subnetting to Meet Requirements
8.1.4.6 – Lab – Calculating IPv4 Subnets

## Slide 51: Subnetting to Meet Requirements Packet Tracer – Subnetting Scenario
Notes: 8.1 – Subnetting an IPv4 Network
8.1.4 – Subnetting to Meet Requirements
8.1.4.7 – Packet Tracer – Subnetting Scenario

## Slide 52: Subnetting to Meet Requirements Lab – Designing and Implementing a Subnetted IPv4 Addressing Scheme
Notes: 8.1 – Subnetting an IPv4 Network
8.1.4 – Subnetting to Meet Requirements
8.1.4.8 – Lab – Designing and Implementing a Subnetted IPv4 Addressing Scheme

## Slide 53: Benefits of Variable Length Subnet Masking Traditional Subnetting Wastes Addresses
Notes: 8.1 – Subnetting an IPv4 Network
8.1.5 – Benefits of Variable Length Subnet Masking
8.1.5.1– Traditional Subnetting Wastes Addresses

## Slide 54: Benefits of Variable Length Subnet Masking Variable Length Subnet Masks (VLSM)
Traditional
Subnets of Varying Sizes
Notes: 8.1 – Subnetting an IPv4 Network
8.1.5 – Benefits of Variable Length Subnet Masking
8.1.5.2 – Variable Length Subnet Masks (VLSM)

## Slide 55: Benefits of Variable Length Subnet Masking Basic VLSM
Basic Subnetting
Notes: 8.1 – Subnetting an IPv4 Network
8.1.5 – Benefits of Variable Length Subnet Masking
8.1.5.3 – Basic VLSM

## Slide 56: Benefits of Variable Length Subnet Masking Video Demonstration – VLSM Basics
Basic VLSM
  Subnets do not have to be equal sizes, as long as their address ranges do not overlap.
  When creating subnets it is easier to work from larger to smaller.
Notes: 8.1 – Subnetting an IPv4 Network
8.1.5 – Benefits of Variable Length Subnet Masking
8.1.5.4 – Video Demonstration – VLSM Basics

## Slide 57: Benefits of Variable Length Subnet Masking VLSM in Practice
Notes: 8.1 – Subnetting an IPv4 Network
8.1.5 – Benefits of Variable Length Subnet Masking
8.1.5.5 – VLSM in Practice

## Slide 58: Benefits of Variable Length Subnet Masking VLSM Chart
Notes: 8.1 – Subnetting an IPv4 Network
8.1.5 – Benefits of Variable Length Subnet Masking
8.1.5.6 – VLSM Chart

## Slide 59: Benefits of Variable Length Subnet Masking Video Demonstration – VLSM Example
Given the network 172.16.0.0 /23 creates subnets:
  1 network for 200 hosts - 256
  1 network for 100 hosts - 128
  1 network for 50 hosts - 64
  1 network for 25 hosts - 32
  1 network for 10 hosts - 16
  4 point-to-point networks for 2 hosts each – 4x4 = 16
/23 = 2^9 hosts = 512
256+128+64+32+16+16 = 512 hosts needed
Address range 172.16.0.0 – 172.16.1.255
172.16.1.248 /30 (4)
172.16.1.252 /30 (4)
Notes: 8.1 – Subnetting an IPv4 Network
8.1.5 – Benefits of Variable Length Subnet Masking
8.1.5.7 – Video Demonstration – VLSM Example

## Slide 60: 8.2 Addressing Schemes
Notes: 8 – Subnetting IP Networks
8.2 – Addressing Schemes

## Slide 61: Structured Design Network Address Planning
Notes: 8.2 – Addressing Schemes
8.2.1 – Structured Design
8.2.1.1 – Network Address Planning

## Slide 62: Structured Design Planning to Address the Network
Each host in an internetwork must have a unique address.
Need proper planning & documentation.
Must provide & control access to servers from internal hosts and external hosts.
Layer 3 STATIC address assigned to a server can be used to control access to that server.
Monitoring security and performance of hosts means network traffic is examined for source IP addresses that are generating or receiving excessive packets.
Notes: 8.2 – Addressing Schemes
8.2.1 – Structured Design
8.2.1.2 – Planning to Address the Network

## Slide 63: Structured Design Assigning Addresses to Devices
Devices that require addresses:
  End user clients
  Can be set for DHCP to save time and manual errors.
  A change in the subnetting scheme requires reconfiguration of DHCP server. IPv6 clients use DHCPv6/SLAAC.
  Servers
    Configured with static addresses.
    Private addresses translated to public addresses if accessible from the Internet.
  Intermediary devices
    Set with static addresses for remote management.
  Gateway
    Router interface used to exit the network.
Notes: 8.2 – Addressing Schemes
8.2.1 – Structured Design
8.2.1.3 – Assigning Addresses to Devices

## Slide 64: Structured Design Packet Tracer – Designing and Implementing a VLSM Addressing Scheme
Notes: 8.2 – Addressing Schemes
8.2.1 – Structured Design
8.2.1.4 – Packet Tracer – Designing and Implementing a VLSM Addressing Scheme

## Slide 65: Structured Design Lab – Designing and Implementing a VLSM Addressing Scheme
Notes: 8.2 – Addressing Schemes
8.2.1 – Structured Design
8.2.1.5 – Lab – Designing and Implementing a VLSM Addressing Scheme

## Slide 66: 8.3 Design Considerations for IPv6
Notes: 8 – Subnetting IP Networks
8.3 – Design Considerations for IPv6

## Slide 67: Subnetting an IPv6 Network The IPv6 Global Unicast Address
Structure
IPv6 subnetting is not concerned with conserving address space.
IPv6 subnetting is about building an addressing hierarchy based on the number of subnetworks needed.
IPv6 link-local address is never subnetted.
IPv6 global unicast address can be subnetted.
IPv6 global unicast address normally consists of a /48 global routing prefix, a 16 bit subnet ID, and a 64 bit interface ID.
Notes: 8.3 – Design Considerations for IPv6
8.3.1 – Subnetting an IPv6 Network
8.3.1.1 – The IPv6 Global Unicast Address

## Slide 68: Subnetting an IPv6 Network Subnetting Using the Subnet ID
Notes: 8.3 – Design Considerations for IPv6
8.3.1 – Subnetting an IPv6 Network
8.3.1.2 – Subnetting Using the Subnet ID

## Slide 69: Subnetting an IPv6 Network IPv6 Subnet Allocation
Notes: 8.3 – Design Considerations for IPv6
8.3.1 – Subnetting an IPv6 Network
8.3.1.3 – IPv6 Subnet Allocation

## Slide 70: Subnetting an IPv6 Network Packet Tracer – Implementing a Subnetted IPv6 Addressing Scheme
Notes: 8.3 – Design Considerations for IPv6
8.3.1 – Subnetting an IPv6 Network
8.3.1.4 – Packet Tracer – Implementing a Subnetted IPv6 Addressing Scheme

## Slide 71: 8.4 Chapter Summary
Notes: 8 – Subnetting IP Networks
8.4 – Summary

## Slide 72: Conclusion Packet Tracer - Skills Integration Challenge
Notes: 8.4 – Summary
8.4.1 – Conclusion
8.4.1.2 – Packet Tracer – Skils Integration Challenge

## Slide 73: Conclusion Chapter 8: Subnetting IP Networks
Implement an IPv4 addressing scheme to enable end-to-end connectivity in a small to medium-sized business network.
Given a set of requirements, implement a VLSM addressing scheme to provide connectivity to end users in a small to medium-sized network.
Explain design considerations for implementing IPv6 in a business network.
Notes: 8.4 – Summary
8.4.1 – Conclusion
8.4.1.3 – Subnetting IP Networks

## Slide 74: Section 8.1– 8.3 New Terms and Commands
octet boundary Variable Length Subnet Masking (VLSM) |  | 
Notes: New Terms and Commands