## Slide 1: Chapter 7: Access Control Lists
CCNA Routing and Switching
Routing and Switching Essentials v6.0
Notes: Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 7: Access Control Lists

## Slide 2: Chapter 7 - Sections & Objectives
7.1 ACL Operation
  Explain the purpose and operation of ACLs in small to medium-sized business networks.
  Explain how ACLs filter traffic.
  Explain how ACLs use wildcard masks.
  Explain how to create ACLs.
  Explain how to place ACLs.
7.2 Standard IPv4 ACLs
  Configure standard IPv4 ACLs to filter traffic in a small to medium-sized business network.
  Configure standard IPv4 ACLs to filter traffic to meet networking requirements.
  Use sequence numbers to edit existing standard IPv4 ACLs.
  Configure a standard ACL to secure VTY access.
Notes: 2
Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 7: Access Control Lists

## Slide 3: Chapter 7 - Sections & Objectives (Cont.)
7.3 Troubleshoot ACLs
  Troubleshoot IPv4 ACL issues.
  Explain how a router processes packets when an ACL is applied.
  Troubleshoot common standard IPv4 ACL errors using CLI commands.
Notes: 3
Cisco Networking Academy Program
Routing and Switching Essentials v6.0
Chapter 7: Access Control Lists

## Slide 4: 7.1 ACL Operation
Notes: 7- Access Control Lists
7.1 – IOS Bootcamp

## Slide 5: Purpose of ACLs What is an ACL?
An ACL is a series of IOS commands that control whether a router forwards or drops packets based on information found in the packet header. ACLs are not configured by default on a router.
ACL's can perform the following tasks:
  Limit network traffic to increase network performance. For example, video traffic could be blocked if it's not permitted.
  Provide traffic flow control. ACLs can help verify routing updates are from a known source.
  ACLs provide security for network access and can block a host or a network.
  Filter traffic based on traffic type such as Telnet traffic.
  Screen hosts to permit or deny access to network services such as FTP or HTTP.
Notes: 7.1 – ACL Operation
7.1.1 – Purpose of ACLs
7.1.1.1 – What is an ACL?

## Slide 6: Purpose of ACLs Packet Filtering
An ACL is a sequential list of permit or deny statements, known as access control entries (ACEs).
  ACEs are commonly called ACL statements.
When network traffic passes through an interface configured with an ACL, the router compares the information within the packet against each ACE, in sequential order, to determine if the packet matches one of the ACEs. This is referred to as packet filtering.
Packet Filtering:
  Can analyze incoming and/or outgoing packets.
  Can occur at Layer 3 or Layer 4.
The last statement of an ACL is always an implicit deny. This is automatically inserted at the end of each ACL and blocks all traffic. Because of this, all ACLs should have at least one permit statement.
Notes: 7.1 – ACL Operation
7.1.1 – Purpose of ACLs
7.1.1.2 – Packet Filtering

## Slide 7: Purpose of ACLs ACL Operation
ACLs do not act on packets that originate from the router itself.
  ACLs define the set of rules that give added control for packets that enter inbound interfaces, packets that relay through the router, and packets that exit outbound interfaces of the router.
ACLs can be configured to apply to inbound traffic and outbound traffic:
  Inbound ACLs – Incoming packets are processed before they are routed to the outbound interface.
  Outbound ACLs – Incoming packets are routed to the outbound interface, and then they are processed through the outbound ACL.
Notes: 7.1 – ACL Operation
7.1.1 – Purpose of ACLs
7.1.1.3 – ACL Operation

## Slide 8: Wildcard Masks in ACLs Introducing ACL Wildcard Masking
IPv4 ACEs require the use of wildcard masks.
A wildcard mask is a string of 32 binary digits (1s and 0s) used by the router to determine which bits of the address to examine for a match.
Wildcard masks are often referred to as an inverse mask since unlike a subnet mask where a binary 1 is a match, a binary 0 is a match with wildcard masks. For example:
Notes: 7.1 – ACL Operation
7.1.2 – Wildcard Masks in ACLs
7.1.2.1 - Introducing ACL Wildcard Masking

## Slide 9: Wildcard Masks in ACLs Wildcard Mask Examples
Calculating the wildcard mask to match IPV4 subnets takes practice. In the first to the left:
  Example 1: The wildcard mask stipulates that every bit in the IPv4 192.168.1.1 address must match exactly.
  Example 2: The wildcard mask stipulates that anything will match.
  Example 3: The wildcard mask stipulates that any host within the 192.168.1.0/24 network will match.
Notes: 7.1 – ACL Operation
7.1.2 – Wildcard Masks in ACLs
7.1.2.2 - Wildcard Mask Examples

## Slide 10: Wildcard Masks in ACLs Calculating the Wildcard Mask
Calculating wildcard mask examples:
  Example 1: Assume you want to permit access to all users in the 192.168.3.0 network with the subnet mask of 255.255.255.0. Subtract the subnet from 255.255.255.255 and the result is: 0.0.0.255.
  Example 2: Assume you want to permit network access for the 14 users in the subnet 192.168.3.32/28 with the subnet mask of 255.255.255.240. After subtracting the subnet maks from 255.255.255.255, the result is 0.0.0.15.
  Example 3: Assume you want to match only networks 192.168.10.0 and 192.168.11.0 with the subnet mask of 255.255.254.0. After subtracting the subnet mask from 255.255.255.255, the result is 0.0.1.255.
Notes: 7.1 – ACL Operation
7.1.2 – Wildcard Masks in ACLs
7.1.2.3 - Calculating the Wildcard Mask

## Slide 11: Wildcard Masks in ACLs Wildcard Mask Keywords
To make wildcard masks easier to read, the keywords host and any can help identify the most common uses of wildcard masking.
    host substitutes for the 0.0.0.0 mask
    any substitutes for the 255.255.255.255 mask
If you would like to match the 192.169.10.10 address, you could use 192.168.10.10 0.0.0.0 or, you can use: host 192.168.10.10
In Example 2, instead of entering 0.0.0.0 255.255.255.255, you can use the keyword any by itself.
Notes: 7.1 – ACL Operation
7.1.2 – Wildcard Masks in ACLs
7.1.2.4 - Wildcard Mask Keywords

## Slide 12: Wildcard Masks in ACLs Wildcard Mask Keyword Examples
Example 1 in the figure demonstrates how to use the any keyword to substitute the IPv4 address 0.0.0.0 with a wildcard mask of 255.255.255.255.
Example 2 demonstrates how to use the host keyword to substitute for the wildcard mask when identifying a single host.
Notes: 7.1 – ACL Operation
7.1.2 – Wildcard Masks in ACLs
7.1.2.5 - Wildcard Mask Keyword Examples

## Slide 13: Guidelines for ACL Creation General Guidelines for Creating ACLs
Use ACLs in firewall routers positioned between your internal network and an external network such as the Internet.
Use ACLs on a router positioned between two parts of your network to control traffic entering or exiting a specific part of your internal network.
Configure ACLs on border routers such as those situated at the edge of your network. This will provide a basic buffer from the outside network that is less controlled.
Configure ACLs for each network protocol configured on the border router interfaces.
Notes: 7.1 – ACL Operation
7.1.3 – Guidelines for ACL Creation
7.1.3.1 - General guidelines for Creating ACLs

## Slide 14: Guidelines for ACL Creation ACL Best Practices
Using ACLs requires significant attention to detail. Mistakes can be very costly in terms of downtime, troubleshooting efforts, and poor network performance.
Notes: 7.1 – ACL Operation
7.1.3 – Guidelines for ACL Creation
7.1.3.2 - ACL Best Practices

## Slide 15: Guidelines for ACL Creation General Guidelines for Creating ACLs
The proper placement of an ACL can make the network operate more efficiently. For example, and ACL can be placed to reduce unnecessary traffic.
Every ACL should be placed where it has the greatest impact on efficiency.
  Extended ACLs – Configure extended ACLs as close as possible to the source of the traffic to be filtered. This will prevent undesirable traffic as close to the source without it crossing the network infrastructure.
  Standard ACLs – Since standard ACLs do not specify destination addresses, they should be configured as close to the destination as possible.
Notes: 7.1 – ACL Operation
7.1.4 – Guidelines for ACL Placement
7.1.4.1 – Where to Place ACLs

## Slide 16: Guidelines for ACL Creation Standard ACL Placement
This example demonstrates the proper placement of the standard ACL that is configured to block traffic from the 192.168.10.0/24 network to the 192.168.30.0/24 network.
There are two possible places to configure the access-list on R3.
If the access-list is applied to the S0/0/1 interface, it will block traffic to the 192.168.30.0/24 network, but also, going to the 192.168.31.0/24 network.
The best place to apply the access list is on R3’s G0/0 interface. The access-list list should be applied to traffic exiting the G0/0 interface. Packets from 192.168.10.0/24 can still reach 192.168.31.0/24.
Notes: 7.1 – ACL Operation
7.1.4 – Guidelines for ACL Placement
7.1.4.2 – Standard ACL Placement

## Slide 17: 7.2 Standard IPv4 ACLs
Notes: 7- Access Control Lists
7.2 – Standard IPv4 ACLs

## Slide 18: Configure Standard IPv4 ACLs Numbered Standard IPv4 ACL Syntax
The access-list global configuration command defines a standard ACL with a number in the range of 1 through 99.
The full syntax of the standard ACL command is as follows:
    Router(config)# access-list access-list-number { deny | permit | remark } source [ source-wildcard ][ log ]
  To remove the ACL, the global configuration no access-list command is used. Use the show access-list command to verify the removal of the ACL.
Notes: 7.2 – Standard IPv4 ACLs
7.2.1 – Configure Standard IPv4 ACLs
7.2.1.1 – Numbered Standard IPv4 ACL Examples

## Slide 19: Configure Standard IPv4 ACLs Applying Standard IPv4 ACLs to Interfaces
After a standard IPv4 ACL is configured, it is linked to an interface using the ip access-group command in interface configuration mode:
  Router(config-if)# ip access-group { access-list-number | access-list-name } { in | out }
To remove an ACL from an interface, first enter the no ip access-group command on the interface, and then enter the global no access-list command to remove the entire ACL.
Notes: 7.2 – Standard IPv4 ACLs
7.2.1 – Configure Standard IPv4 ACLs
7.2.1.2 – Applying Standard IPv4 ACLs to Interfaces

## Slide 20: Configure Standard IPv4 ACLs Numbered Standard IPv4 ACL Examples
The figure to the left shows an example of an ACL that permits traffic from a specific subnet but denies traffic from a specific host on that subnet.
  The no access-list 1 command deletes the previous version of ACL 1.
  The next ACL statement denies the host 192.168.10.10.
  What is another way to write this command without using host?
  All other hosts on the 192.168.10.0/24 network are then permitted.
  There is an implicit deny statement that matches every other network.
  Next, the ACL is reapplied to the interface in an outbound direction.
Notes: 7.2 – Standard IPv4 ACLs
7.2.1 – Configure Standard IPv4 ACLs
7.2.1.3 – Numbered Standard IPv4 ACL Examples

## Slide 21: Configure Standard IPv4 ACLs Numbered Standard IPv4 ACL Examples (Cont.)
This next example demonstrates an ACL that denies a specific host but will permit all other traffic.
  The first ACL statement deletes the previous version of ACL 1.
  The next command, with the deny keyword, will deny traffic from the PC1 host that is located at 192.168.10.10.
  The access-list 1 permit any statement will permit all other hosts.
  This ACL is applied to interface G0/0 in the inbound direction since it only affects the 192.168.10.0/24 LAN.
Notes: 7.2 – Standard IPv4 ACLs
7.2.1 – Configure Standard IPv4 ACLs
7.2.1.3 – Numbered Standard IPv4 ACL Examples

## Slide 22: Configure Standard IPv4 ACLs Named Standard IPv4 ACL Syntax
Identifying an ACL with a name rather than with a number makes it easier to understand its function.
The example to the left shows how to configured a named standard access list. Notice how the commands are slightly different:
  Use the ip access-list command to create a named ACL. Names are alphanumeric, case sensitive, and must be unique.
  Use permit or deny statements as needed. You can also use the remark command to add comments.
  Apply the ACL to an interface using the ip access-group name command.
Notes: 7.2 – Standard IPv4 ACLs
7.2.1 – Configure Standard IPv4 ACLs
7.2.1.4 – Named Standard IPv4 ACL Syntax

## Slide 23: Modify IPv4 ACLs Method 1 – Use a Text Editor
It is sometimes easier to create and edit ACLs in a text editor such as Microsoft Notepad rather making changes directly on the router.
For an existing ACL, use the show running-config command to display the ACL, copy and paste it into the text editor, make the necessary changes, and then paste it back in to the router interface.
It is important to note that when using the no access-list command, different IOS software releases act differently.
  If the ACL that has been deleted is still applied to the interface, some IOS versions act as if no ACL is protecting your network while others deny all traffic.
Notes: 7.2 – Standard IPv4 ACLs
7.2.2 – Modify IPv4 ACLs
7.2.2.1 – Method 1 – Use a Text Editor

## Slide 24: Modify IPv4 ACLs Method 2 – Use Sequence Numbers
The figure to the left demonstrates the steps used to make changes to a numbered ACL using sequence numbers.
Step 1 identifies the problem. The deny 192.168.10.99 statement is incorrect. The host to deny should be 192.168.10.10
To make the edit, Step 2 shows how to go into standard access-list 1 and make the change. The misconfigured statement had to be deleted with the no command: no 10
Once it was deleted, the new statement with the correct host was added: 10 deny host 192.168.10.10
Notes: 7.2 – Standard IPv4 ACLs
7.2.2 – Modify IPv4 ACLs
7.2.2.2 – Method 2 – Use Sequence Numbers

## Slide 25: Modify IPv4 ACLs Editing Standard Named ACLs
By referring to statement sequence numbers, individual statements can be easily inserted or deleted.
The figure to the left shows an example of how to insert a line into a named ACL.
By numbering it 15, it will place the command in between statement 10 and 20.
Please notice that when the ACL was originally created, the network administrator spaced each command by 10 which left room for edits and additions.
The no sequence-number named ACL command is used to delete individual statements.
Notes: 7.2 – Standard IPv4 ACLs
7.2.2 – Modify IPv4 ACLs
7.2.2.3 – Editing Standard Named ACLs

## Slide 26: Modify IPv4 ACLs Verifying ACLs
Use the show ip interface command to verify that the ACL is applied to the correct interface.
The output will display the name of the access list and the direction in which it was applied to the interface.
Use the show access-lists command to display the access-lists configured on the router.
Notice how the sequence is displayed out of order for the NO_ACCESS access list. This will be discussed later in this section.
Notes: 7.2 – Standard IPv4 ACLs
7.2.2 – Modify IPv4 ACLs
7.2.2.4 – Verifying ACLs

## Slide 27: Modify IPv4 ACLs ACL Statistics
The show access-lists command can be used to display matched statistics after an ACL has been applied to an interface and some testing has occurred.
When traffic is generated that should match an ACL statement, the matches shown in the show access-lists command output should increase.
Recall that every ACL has an implicit deny any as the last statement. The statistics for this implicit command will not be displayed. However, if this command is configured manually, the results will be displayed.
The clear access-list counters command can be used to clear the counters for testing purposes.
Notes: 7.2 – Standard IPv4 ACLs
7.2.2 – Modify IPv4 ACLs
7.2.2.5 – ACL Statistics

## Slide 28: Securing VTY ports with a Standard IPv4 ACL The access-class Command
Administrative VTY access to Cisco devices should be restricted to help improve security.
Restricting VTY access is a technique that allows you define which IP addresses are allowed remote access to the router EXEC process.
The access-class command configured in line configuration mode will restrict incoming and outgoing connections between a particular VTY (into a Cisco device) and the addresses in an access list.
Router(config-line)# access-class access-list-number {in [vrf-also ] | out }
Notes: 7.2 – Standard IPv4 ACLs
7.2.3 – Securing VTY ports with a Standard IPv4 ACL
7.2.3.1 – The access-class Command

## Slide 29: Securing VTY ports with a Standard IPv4 ACL Verifying the VTY Port is Secured
Verification of the ACL configuration used to restrict VTY access is important.
The figure to the left shows two devices trying to ssh into two different devices.
The show access-lists command output shows the results after the SSH attempts by PC1 and PC2.
Notice the match results in the permit and the deny statements.
Notes: 7.2 – Standard IPv4 ACLs
7.2.3 – Securing VTY ports with a Standard IPv4 ACL
7.2.3.2 – Verifying the VTY Port is Secured

## Slide 30: 7.3 Troubleshoot ACLs
Notes: 7- Access Control Lists
7.3 – Troubleshoot ACLs

## Slide 31: Processing Packets with ACLs The Implicit Deny Any
A single-entry ACL with only one deny entry has the effect of denying all traffic.
At least one permit ACE must be configured in an ACL or all traffic will be blocked.
Study the two ACLs in the figure to the left.
  Will the results be the same or different?
Notes: 7.3 – Troubleshoot ACLs
7.3.1 – Processing Packets with ACLs
7.3.1.1 – The Implicit Deny Any

## Slide 32: Processing Packets with ACLs The Order of ACEs in an ACL
The order in which ACEs are configured are important since ACEs are processed sequentially.
The figure to the left demonstrates a conflict between two statements since they are in the wrong order.
  The first deny statement blocks everything in the 192.168.10.0/24 network.
  However, the second permit statement is attempting to allow host 192.168.10.10 through.
  This statement is rejected since it is a subset of the previous statement.
  Reversing the order of these two statements will solve the problem.
Notes: 7.3 – Troubleshoot ACLs
7.3.1 – Processing Packets with ACLs
7.3.1.2 – The Order of ACEs in an ACL

## Slide 33: Processing Packets with ACLs Cisco IOS Reorders Standard ACLs
Note the order in which the access-list statements were entered during configuration.
Notice how the order was changed when you enter the show running-config command.
The host statements are listed first, however, not in the order they were entered.
The IOS puts host statements in an order using a special hashing function. The resulting order optimizes the search for a host ACL entry.
The range statements are displayed in the order they were entered. The hashing function is applied to host statements.
Notes: 7.3 – Troubleshoot ACLs
7.3.1 – Processing Packets with ACLs
7.3.1.3 – Cisco IOS Reorders Standard ACLs

## Slide 34: Processing Packets with ACLs Routing Processes and ACLs
The figure shows the logic of routing and ACL processes.
When a packet arrives at a router interface, the router process is the same, whether ACLs are configured or not.
After the frame information is stripped off, the router checks for an ACL on the inbound interface. If an ACL exists, the packet is tested against the statements.
If the packet matches a statement, the packet is either permitted or denied.
If the packet is permitted, and after the router processes the packet, the outgoing interface will also be checked for an ACL.
Notes: 7.3 – Troubleshoot ACLs
7.3.1 – Processing Packets with ACLs
7.3.1.4 – Routing Processes and ACLs

## Slide 35: Common IPv4 Standard ACL Errors Troubleshooting Standard IPv4 ACLs – Example 1
The most common errors involving ACLs:
  Entering ACEs in the wrong order
  Not specifying adequate ACL rules
  Applying the ACL using the wrong direction, wrong interface, or wrong source address
In the figure to the left, PC2 should not be able to access the File Server. However, PC1 can not access it either.
The output of the show access-list command shows the one deny statement in the ACL.
The set of commands on the right shows the solution. The permit statement allows other devices to access since the implicit deny was blocking other traffic.
Notes: 7.3 – Troubleshoot ACLs
7.3.2 – Common IPv4 Standard ACL Errors
7.3.2.1 – Troubleshooting Standard IPv4 ACLs – Example 1

## Slide 36: Common IPv4 Standard ACL Errors Troubleshooting Standard IPv4 ACLs – Example 2
The 192.168.11.0/24 network should not be able to access the 192.168.10.0/24 network.
PC2 cannot access PC1 as planned, however, it also cannot access the Internet through R2.
Problem: access-list 20 was applied to G0/1 on an inbound direction
Where should ACL 20 be applied and in which direction?
In order for PC2 to access the Internet, ACL 20 needs to be removed from the G0/1 interface and applied outbound on the G0/0 interface.
Notes: 7.3 – Troubleshoot ACLs
7.3.2 – Common IPv4 Standard ACL Errors
7.3.2.2 – Troubleshooting Standard IPv4 ACLs – Example 2

## Slide 37: Common IPv4 Standard ACL Errors Troubleshooting Standard IPv4 ACLs – Example 3
Only PC1 should be allowed to SSH to R1.
There is a problem with the config in the figure to the left since PC1 is unable to SSH to R1.
The ACL is permitting the 192.168.10.1 address which is the G0/0 interface. However, the address that should be permitted is the PC1 host address of 192.168.10.10.
The solution is provided below:
Notes: 7.3 – Troubleshoot ACLs
7.3.2 – Common IPv4 Standard ACL Errors
7.3.2.3 – Troubleshooting Standard IPv4 ACLs – Example 3

## Slide 38: Common IPv4 Standard ACL Errors Packet Tracer – Troubleshooting Standard IPv4 ACLs
This Packet Tracer activity will require the troubleshooting of various IPv4 ACL issues.
Notes: 7.3 – Troubleshoot ACLs
7.3.2 – Common IPv4 Standard ACL Errors
7.3.2.4 – Packet Tracer - Troubleshooting Standard IPv4 ACLs

## Slide 39: 7.4 Chapter Summary
Notes: 7 – Access Control Lists
7.4 – Summary

## Slide 40: Securing VTY ports with a Standard IPv4 ACL Packet Tracer – Skills Integration Challenge
This Packet Tracer activity will require you to finish the IP addressing scheme, configure routing, and implement named access control lists.
Notes: 7.4 – Summary
7.4.1 – Conclusion
7.4.1.2 – Packet Tracer – Skills Integration Challenge

## Slide 41: Chapter 7 New Terms and Commands
access control lists (ACLs) firewalls access control entries (ACEs) packet filtering Standard ACLs Extended ACLs implicit deny Inbound ACLs Outbound ACLs wildcard masks named ACLs inverse mask | 
Notes: New Terms and Commands